## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Designing for Reduced Hazard
Image: Wikimedia Commons, Fume Hood , Author: U.S. National Institute for Occupational Safety and Health
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 2
Hazard and Risk – Past and Present
Toxicology
Assessing Hazards and Exposure
  What Happens When You’re Exposed?
Hazard Minimization Through Molecular Design
QSAR - Quantitative Structure Activity Relationship
Molecular Design Research Network (MoDRN)
Topics To Be Covered

## Slide 3
There are over 100,000 chemicals in global circulation.
> 700 chemicals are introduced to the US market each year.
85% of these chemicals lack experimental data on environmental risk.
There has been unintended biological activity which has led to increased hazard as well as toxic endpoints for humans and the environment.
The Challenge of Environmental Risk
Source: Wikimedia Commons

## Slide 4
The ability cause adverse consequence.
What types of chemical hazards are there?
  Global Hazards (global warming, acid rain, security threat, ozone depletion)
  Physicochemical Hazards (explosivity, corrosivity, oxidizers/reducers)
  Toxicological
    Environmental (aquatic toxicity, avian toxicity, mammalian toxicity)
    Human (e.g., carcinogenicity, neurotoxicity, hepatotoxicity, dermal toxicity)
Hazard

## Slide 5
risk = f (hazard, exposure)
Risk to the environment stems from exposure to a potential environmental hazard
Two routes to reduce risk:
If hazard , exposure needs to be reduced to 0
If hazard = 0, exposure can be
Ultimate goal is to use BENIGN materials = no hazard!
The Risk Equation
 Exposure becomes irrelevant
 Less dependence on systems which can fail or be sabotaged
 Competitive advantage – reduces costs associated with toxic materials
conventional strategy: wear PPE!
aim of Green Chemistry

## Slide 6
Dealing with waste: treatment, control, disposal; pollutant monitoring; hazardous waste site cleanup.
Development of standards for emissions to air, releases to water, and disposal by land, as well as regulation of these standards.
“Command and Control”
Compensating injured employees
Investment in protective equipments
Historical Approach to Hazard Problems

## Slide 7
In 2011, in USA only, 1.78  106 tons of toxic chemicals were released directly to air, water and land
Only 650 toxic chemicals/chemical categories (out of 100,000 in commerce) are tracked by Toxic Release Inventory
Mihelcic & Zimmerman, Environmental engineering: Fundamentals, sustainability, design. Wiley Global Education (2014).
Chemicals in the Environment
...meanwhile in the EU...
REACH is a 2007 regulation of the European Union
Registration, Evaluation, Authorisation & Restriction of Chemicals
Goals:
   to improve the protection of human health and the environment from the risks that can be posed by chemicals.
   to promote alternative methods for the hazard assessment of substances in order to reduce the number of tests on animals.
Companies need to register their substances - to do this they need to work together with other companies who are registering the same substance.

## Slide 8
One of Green Chemistry’s greatest strengths is the ability to design for reduced hazard.
148 xenobiotics in the body
Xenobiotic: synthetic chemical, that is foreign to the body or to an ecological system.
Of the chemicals found:
  76 cause cancer in humans or animals,
  94 are toxic to the brain and nervous system, and
  79 cause birth defects or abnormal development.
The dangers of exposure to these chemicals in combination has never been studied.
Image Source: http://svtc.org/our-work/e-waste/
Why is This Relevant?

## Slide 9
The traditional definition of toxicology is "the science of poisons."
A more descriptive definition of toxicology is
"the study of the adverse effects of chemicals or physical agents on living organisms".
What is Toxicology?

## Slide 10
What Counts as Toxic
Mihelcic & Zimmerman, Environmental engineering: Fundamentals, sustainability, design. Wiley Global Education (2014).
A toxic agent is anything that can produce an adverse biological effect;
it may be chemical, physical, or biological in form.
chemical (such as cyanide),
physical (such as radiation), and
biological (such as snake venom)

## Slide 11
Acute toxicity | Carcinogenicity | Bioconcentration
Subchronic & chronic toxicity | Neurotoxicity | Degradation & transport
Reproductive toxicity | Immunotoxicity | Aquatic toxicity
Developmental toxicity | Genotoxicity | Terrestrial organism toxicity
Molecular weight | Molecular volume | Dipole moment
Hydrophilic surface area | Hydrophobic surface area | Rotatable bonds
Hydrogen bonds | Ionization potential | Electron affinity
Partition coefficients | Acid/base properties | Polarizability
Relating Toxic Endpoints to Molecular Features & Properties
Relationships

## Slide 12: What is the most important factor in bringing about the adverse biological impact?
Dose
the amount of a substance administered at given times.
examples:
  650 mg Tylenol as a single dose
  500 mg Penicillin every 8 hours for 10 days
Highly toxic chemicals can be life saving when given in appropriate doses.
An apparently nontoxic chemical can be toxic at high doses.
Too much of a good thing can hurt you!
Source: Wikimedia Commons

## Slide 13
Source: Marczewski, A.E., and Kamrin, M. Toxicology for the citizen, Retrieved August 17, 2000: www.iet.msu.edu/toxconcepts/toxconcepts.htm.
Approximate Lethal Doses of Common Chemicals (Calculated for a 100 kg human from data on rats)
Chemical Lethal Dose
Sugar (sucrose) 900 g
Alcohol (ethyl alcohol) 1.5 L
Salt (sodium chloride) 250 g
Herbicide (2, 4-D) 125 mL
Arsenic (arsenic acid) 1-2 teaspoons
Nicotine one half teaspoon
Food poison (botulinum toxin) microscopic
Lethal Doses

## Slide 14: How is toxicity testing done?

## Slide 15
The dose-response relationship is a fundamental and essential concept in toxicology. It correlates exposures and the spectrum of induced effects.
The dose-response relationship is based on observed data from
 experimental animal studies
 human in vitro cell studies
 human clinical studies (but for drugs only!)
Dose-Response
Dose-response assessment is a step in the risk assessment process (Image Source: ORAU, ©)

## Slide 16
Knowledge of the dose-response relationship:
 establishes causality between dose exposure and the observed effects
 establishes the lowest dose where an induced effect occurs - the threshold effect
 determines the rate at which injury builds up - the slope for the dose response.
Dose-Response
LD 50
RfD – estimate of a daily oral exposure to the human population, that’s likely to be without risk of an effect.
UF = Uncertainty factor (usually 10-1000)
UF is bigger when larger uncertainty on experiment
LD 50- estimate for acute toxicity is the Lethal Dose Response 50%; a statistically derived dose at which 50% of the individuals will be expected to die.
NOAEL - No Observed Adverse Effect Level
Highest observed data point with no adverse effect
LOAEL - Low Observed Adverse Effect Level
Lowest data point with an adverse effect
Relevant Metrics

## Slide 17
0
100
50
40
30
20
10
60
70
80
90
Inhaled Dose (ppm)
% Mortality
Solvent 99-7
Solvent 99-2
0 50 100 150 200 250 300 350
Plotted here are two theoretical curves for the toxicity of solvents used in the cleaning of silicon compounds. Both solvent 99-2 and 99-7 performed equally well against a variety of manufactured silicon compounds. The task at hand for you is to determine which solvent would you pick to be “safer” for use. As you can see from the accompanying data both compounds have an equivalent Lethal dose 50 value (LD50). These are based on average values during a 6 hour exposure period.
In-Class Discussion- Which Solvent Would You Use?

## Slide 18
Solvent 99-7 causes lethality at much lower levels than 99-2 (20ppm versus 100ppm respectively), and the response is much more predictable (i.e. less population heterogeneity). Solvent 99-2 because higher levels can be inhaled before any harmful effects should begin.
0
100
50
40
30
20
10
60
70
80
90
Inhaled Dose (ppm)
% Mortality
Solvent 99-7
Solvent 99-2
0 50 100 150 200 250 300 350
In-Class Discussion- Which Solvent Would You Use?

## Slide 19
Review and analysis of toxicology data and assessing if the substance causes toxic effects
Sources include animal and human studies and computational data
These studies have difficulty with showing causation (if a risk factor lead to disease)
Hazard Assessment
risk = f (hazard, exposure)
Mihelcic & Zimmerman, Environmental engineering: Fundamentals, sustainability, design. Wiley Global Education (2014).

## Slide 20
Determines the extent and frequency of human exposure to target chemicals.
Guidelines for residential, industrial and commercial sites
For engineers, the knowledge of hazard and exposure provides information whether the site needs to be remediated.
Exposure Assessment
Example of exposure evaluation: workers touching soil
risk = f (hazard, exposure)
Mihelcic & Zimmerman, Environmental engineering: Fundamentals, sustainability, design. Wiley Global Education (2014).

## Slide 21: Hazard assessment, dose-response & exposure assessment
Risk Characterization

## Slide 22
ChemHAT - easy way to access summarized information on chemical hazards in the workplace
ChemSpider
Protox
Safer Choice - for consumers, businesses, and purchasers to find products that perform and are safer for human health and the environment.
toxicity assessment based on experimental or predicted LD50
Tools For Hazard Characterization
Notes: Show tools

## Slide 23: What happens once you are exposed to a toxicant?

## Slide 24
ABSORBTION
DISTRIBUTION
METABOLISM
EXCRETION
ADME
http://blog.gyrosproteintechnologies.com/spinblog/adme-of-therapeutic-proteins
Place where the drug (or chemical) can take effect
From: Wang and Skolnik, Chemistry and Biodiversity (2009)
Chemical Processes in ADME

## Slide 25
Dermal
Respiratory
Digestive
Skin is the first barrier to absorption for the chemical. The skin can keep chemicals out of the body, or it can let them in, depending on the physical and chemical properties of the chemical. Absorption of a chemical will result in the chemical circulating inside the body and perhaps causing adverse effects.
As chemicals are inhaled, they may reach the lungs. The lung surface is a poor barrier against the entry of many chemicals into the body, which means that absorption of chemicals into the lung can be rapid and efficient.
If chemicals are swallowed, either intentionally or unintentionally, they enter the gastrointestinal tract (GI). From there, they may either pass through the body or be absorbed into the body.
Absorption

## Slide 26
Dermal
Respiratory
Digestive
Absorption
Parameter | Preferred | Not Preferred
Physical state | solid | liquid
LogP | Under 0 or greater than 5 | Between 0 and 5
Molecular weight | Over 400 Da | Below 400 Da
Parameter | Preferred | Not Preferred
Particle size | Over 5 nm | Under 5 nm
LogP | Less than 0 or greater than 5 | Between 0 and 5
Mw | Over 400 Da | Under 400 Da
pvapor [mmHg] | Under 0.001 | Over 0.001
Parameter | Preferred | Not Preferred
Particle size | Over 100 nm | Under 100 nm
LogP | Under 0 or above 5 | Between 0-5
Phase | solid | liquid
MW | Over 500 Da | Under 400 Da

## Slide 27
Distribution is the movement of a chemical throughout the bloodstream and into other organs, such as the brain and the bones. Pharmaceuticals such as antibiotics and painkillers are designed to have high distribution rates so they can reach their target organs and have therapeutic effects. For chemicals such as detergents, distribution should be limited.
Distribution depends on many factors such as log P, polar surface area, acidic/basic properties, and molecular weight.
Distribution as opposed to absorption is more difficult to control.
Distribution
Courtesy of Molecular Design Research Network and Dr. Karolina Mellor

## Slide 28
As a chemical is distributed through the body, it will most likely undergo metabolism. Metabolism is the body’s way of transform the molecules into metabolites in the liver. This facilitates their excretion (removal) through the kidneys. The rate at which a chemical is metabolized is usually dependent on its accessibility to enzymes.
Metabolism is unpredictable. Metabolism can lead to detoxification or toxification of the organism.
Metabolism
Courtesy of Molecular Design Research Network and Dr. Karolina Mellor

## Slide 29
After the chemical is absorbed, the body can eliminate it by a process called excretion which can occur through the kidneys, the skin, the GI tract, and the lungs. If the chemical is not eliminated from the body, it can accumulate, or stay in the blood, which can lead to disease. Bioaccumulation is favored for lipophilic molecules in fatty tissues.
Excretion as opposed to absorption is more difficult to control.
Elimination
Courtesy of Molecular Design Research Network and Dr. Karolina Mellor

## Slide 30
Go to chemspider.com and search for acetone
Using discussed parameters, predict respiratory, dermal and digestive absorption of compounds.
What is a likely route for an acetone exposure?
In-Class Exercise

## Slide 31
DERMAL | 
 | acetone
LogP | 
Molecular weight [g/mol] | 
Phase | 
RESPIRATORY | 
 | acetone
LogP | 
Molecular weight [g/mol] | 
Vapor pressure [mmHg] | 
DIGESTIVE | 
 | acetone
LogP | 
Molecular weight [g/mol] | 
Phase | 

## Slide 32
DERMAL | 
 | acetone
LogP | -0.24
Molecular weight [Da] | 58
Phase | liquid
RESPIRATORY | 
 | acetone
LogP | -0.24
Molecular weight [Da] | 58
Vapor pressure [mmHg] | 348.4±0.1
DIGESTIVE | 
 | acetone
LogP | -0.24
Molecular weight [Da] | 58
Phase | liquid

## Slide 33
Acetone is volatile–it will absorb through the respiratory system.
It’s not likely to absorb through membranes.
Since it is a liquid, it will absorb easier than solid.
Conclusions

## Slide 34
Pollution
Persistence
Depletion of resources
Flammability
Radioactivity
Risk of Explosion
Chemical Reactivity
Understanding Physicochemical Properties Associated with Reduced Hazard
Chemical and Physical Properties
pKa chain branching log P molecular refractivity mol. wt. hydrolyzable groups
EHOMO ELUMO electronegativity hardness dipole log D7.4 # H-bond accep/donor
DESIGN
DESIGN

## Slide 35
Absorption organs
GI tract
Skin
Lungs
Eyes
Acidic substance
pKa<7
Unionized at pH>pKa
Basic substance
pKa>7
Un-ionized at pH>pKa
Lipid soluble
Absorbed across intestine membrane intoblood
Chemical
Property-Based Guidelines for Bioavailability
Notes: Different absorption mechanisms - GI tract has largest SA, resp has largets blood flow & thinnest membrane, skin has variable thicknes; different requirements for water sol

## Slide 36
 molecular size < 400 Da
 log Pow 0 - 6
 presence of solvents
 ionization (polar, ionized)
 molecular size < 500 Da
 log Pow 0 - 5
 Non-ionization at GI pH
 particle size < 5um
 molecular size < 400 Da
 vapor pressure < 0.001 mmHg
 water solubility molecular size
 vapor pressure < 0.001 mmHg
Voutchkova et al., Chem. Rev. 2010, 110, 5845.
Property-Based Guidelines for Bioavailability
Absorption organs
GI tract
Skin
Lungs
Eyes

## Slide 37
Educational game based on ADME and scientific data for surfactants to make connection between physico-chemical properties and health.
http://gwiz.yale.edu
For Additional Practice: Safer Chemical Design Game
Courtesy of Molecular Design Research Network and Dr. Karolina Mellor

## Slide 38: Approaches to Hazard Minimization through Molecular Design

## Slide 39
Bioavailability Structure/Shape Activity Mechanism of Action
Molecular
Weight
Solubility
Electronic
Charge
Volatility
Reactive
Functional
Groups
Bioaccumulation/
Persistence
Particle
size
Receptor
binding
Key events
Shape/
Molar Volume
Toxicokinetics
Toxicodynamics
Chemists can control quite well
Not well understood and relatively complex
That’s what we want to target
Green Chemistry Molecular Design Pyramid

## Slide 40
Elimination of the molecular initiating event that activates pathway
Changing reactive functional groups
Reducing or eliminating bioavailability
Reduction of need for associated hazardous substances
Design for End-of-Use product life
Approaches to Hazard Minimization Through Molecular Design

## Slide 41
Where the mechanistic pathway of action is known, molecular structures can be designed such that the necessary reactions are either impossible or highly disfavored: resulting in significant toxicity reduction.
Elimination of the molecular initiating event that activates pathway
Chemical
Properties
Receptor/Ligand
Interaction
DNA Binding
Protein Oxidation
Gene activation
Protein production
Altered signaling
Altered physiology
Disrupted homeostasis
Altered tissue development/ function
Lethality
Impaired
Development
Impaired
Reproduction
Toxicant
Cellular
Responses
Organ
Responses
Organism
Responses
Structure
Recruitment
Extinction
Population
Responses
Macro-Molecular
Interactions
Molecular
Cellular
Tissue
Organ
Organ System
Individual
Population
Ecosystem
Ankley et al. 2010 ET&C; Source: Gary Ankley & Dan Villeneuve, EPA

## Slide 42
In the absence of specific mechanistic information, chemists can modify structure such that certain reactive functional groups, e.g., cyano, electrophilic, etc., can be minimized or eliminated from the chemical structure where feasible.
B. Changing Reactive Functional Groups

## Slide 43
In order for a chemical to manifest its intrinsic hazard, it must be able to reach the toxicological target, human, animal, environmental or global. Through structural molecular design, properties such as solubility, log Kow, and volatility can adjusted to reduce hazard manifestation.
C. Reducing or Eliminating Bioavailability

## Slide 44
Many chemical substances, if not hazardous themselves, require the use of other hazardous substances e.g., paints with VOCs, surfaces requiring specific cleaners, plastics with various additives.
Through molecular design, these associated substances can be eliminated by making the desired properties integral to the product
D. Reduction of Need for Associated Hazardous Substances

## Slide 45
Persistence of chemical in the environment is a problem that can be designed out of molecular structure.
By creating products that degrade to innocuous by-products under designed conditions, e.g., heat, light, time one a can reduce or eliminate this hazard.
Design for utilization of waste as a feedstock is an important goal.
E. Design for End-of-Useful Product Life

## Slide 46: By Changing the Molecular Charge: Cephalosporins
Clinical nephrotoxicity was recognized early – damage to proximal tubular epithelia.
Rapidly transported across basolateral membrane via the organic anion transporter, OAT1. Transport out of cell into lumen is less well characterized (involves other OAT, OAT4).
Cephalosporin has a very low affinity for OAT4 due to its zwitterionic character, resulting in considerable intracellular accumulation
Cephaloridine
Cephalothin
In contrast, cephalothin, an anionic analog of the original zwitterionic drug, rapidly moves across the epithelia from blood into urine
Is thus not a neurotoxin
Cephalosporins: Antibiotic molecules used for gram+ bacteria
Notes: Cephalosporins are a type of beta-lacatam antibiotic.
First generation:Cephaloridine

## Slide 47
Diquat
Paraquat
By Manipulating Sterics: Paraquat and Diquat
Diquats and Paraquats are herbicides (plant killer), primarily for weed and grass control
In animal studies, diquat causes mild, reversible injury
Paraquat is not metabolized by the liver. It has life-threatening effects on the gastrointestinal tract, kidney, liver, heart and other organs
Both: Toxic doses are life threatening. Impacts GI tract, kidney lungs, liver, heart, other organs
Registered as a restricted use pesticide
Not registered as a restricted use pesticide
http://npic.orst.edu/RMPP/rmpp_ch12.pdf
Notes: Paraquat is s non-selective contact herbicide of the diphenyl class. It was introduced in the 1960s and became used worldwide.
However it was soon recognized that paraquat also cause selective pulmonary toxicity to humans (damage to alveolar cells type I and II, causing edema, inflammation and hermorrhage, lung fibrosis).

## Slide 48
Polyethoxylatednonylphenols
Emulsifiers, surfactants
When n = 14-19, intense myocardial necrosis at 40 mg/kg day in dogs and guinea pigs
When n<14 or n>19, no myocardial effects
Glycidyl ethers
When n = 7-9, mutagenic, cause testicular lesions
When n = 11-13+, non-mutagenic
Nonylphenols and Glycidyl Ethers

## Slide 49
Acrylate is understood to be carcinogenic because it can readily undergo Michael addition reactions
The addition of a methyl group to form methacrylate decreases the electrophilicity of the b-carbon, and decreases tendency for Michael reactions.
While this does not reduce the commercial efficacy, but whereas acrylate causes cancer is experimental assays, methacrylate does not.
Acrylate
carcinogenic
Methacrylate
non-carcinogenic
By Manipulating Electrophilicity: Acrylates
Notes: Electr

## Slide 50
Benzene is known to cause hematotoxicity and leukemia in humans
This is understood to be due to one of its metabolites, (E,E)-muconaldehyde.
Toluene is comparatively much less toxic, as the methyl group is oxidized more easily than the benzene ring to give benzoic acid
By Facilitating Detoxification: Benzene
hematotoxicity,
leukemia
non-toxic
hepatic oxidation
[detoxification]

## Slide 51
DDT is well known to be environmentally persistent
DDT analog with Silicon above was synthesized.
While less persistent, the analog turned out to be non-toxic to insects
This is due to the more readily oxidized (metabolized) Si-H bond compared to C-H and also the larger size of the molecule
DDT
(Toxic to insects)
Si-DDT Analog
(Non-toxic to insects)
By Isosteric Substitution: Carbon with Silicon

## Slide 52
Even if chemists design one chemical, it has to undergo tests
Designing New Molecules is Not a Trivial Task

## Slide 53
QSAR = classification models used in the chemical and biological sciences and engineering
QSAR-Quantitative Structure Activity Relationship
Wikipedia
potency of the response variable
"predictor" variables
QSAR
Structure, physico-chemical properties, chemical functionalities
Biological activity: toxicology and eco-toxicology
[like LC50 or oxidative stress]
Known data sets
QSAR established relationship
"predictor" variables
New molecules
QSAR uses the learnt rules to predict biology
QSAR
QSAR predicted potency of the response variable

## Slide 54
A simple QSAR example with 2 parameters
Kostal et al. "Identifying and designing chemicals with minimal acute aquatic toxicity." Proc. Nat. Acad. Sci. 2015, 112, 6289-6294.
Scatter plot colored by category of concern for acute aquatic toxicity based on a 48-h toxicity assay of Daphnia magna
octanol-water distribution coefficient at pH 7.4 (logDo/w)
energy difference between the highest occupied and lowest unoccupied frontier orbitals. ΔE (eV)
In this example a correlation between two parameters: energy gap (ΔE) in molecule and logDow and toxicity for Daphnia is established.
This tool can predict aquatoxicity using a parameter easy to measure (logDow) and a parameter easy to compute (ΔE)
Safe region

## Slide 55
Prediction accuracy not higher than 65-70% for non-carcinogenic chemicals.
Lack of validation with up-to-date data
Application to a narrow range of chemical structures
Qualitative output
Current limitations
Examples of Popular Toxicity Prediction Tools

## Slide 56
Small molecules
Whole organisms
Polypeptide
DNA strands
Enzymes
Receptors
Genes
Organelles
Cells
Tissues
Organs
System size
Toxicology
Computational chemistry
As toxicology has increased its understanding of underlying biological processes leading to toxicity, computational chemistry can now describe the chemical transformations involved in these processes
Next generation: powers of computational Chemistry
Advances in technology & science
Notes: Jakub’s slide

## Slide 57
Next generation: powers of computational Chemistry
Docking software have been able to model very precisely the active site of a target enzyme (target to a drug for instance, or to a toxic).
In drug design such software are used to predict the best molecules for biological activity. Only the best performing are synthesized and tested.
Similar ideas can be used in toxicology
http://www.molfunction.com/software5.htm
Notes: Jakub’s slide

## Slide 58
Create a reliable tool for chemists which will not only predict the toxicity of existing chemicals but will allow a design of future molecules with reduced hazard

## Slide 59
Toxicology
Chemistry
Molecular Biology
Computational Chemistry
Molecular Design Research Network
Notes: MoDRN is the collaboration between 4 universities Baylor, GW, UWASH and Yale that uses advances in biology, toxicology, computational chemistry and engineering to develop a robust and well validated computer software that will not only predict toxicity of existing compounds but it will serve as a tool to redefine guidelines for the next generation molecules with reduced hazard. Our network will employ the newest strategies of computer modeling to build a computer software which will allow to understand what causes toxic endpoints and what can we do to avoid it. Our efforts will not only limit to research. To have the biggest possible impact we will engage educators and students on undergraduate and high school level to by including safer chemical design in students’ lesson plans and by developing interactive and hands-on teaching tools for undergraduate and high school students. Finally we plan to work with our colleagues across academia, colleagues across many industry sectors and policymakers on the government level to further inform and disseminate safe chemical concepts.

## Slide 60
EPA ToxCast
Tox21
Network lab assays
Where is Data Coming from?
High throughput assay
Low throughput assay
National Center for Computational Toxicology (NCCT)

## Slide 61
Assay can test almost any biological effect
In vitro assay in cell
In vivo assay outcome in organism
Ideal assay is:
Reproducible: same result when repeated
Reliable: same result with different people repeat it
Sensitive: won’t miss an effect
Specific: won’t say there is an effect if there is not
Predictive of outcome of interest
What is an Assay?

## Slide 62
Set | Chemicals | Assays | Endpoints | Completion | Available
ToxCast Phase I | 293 | ~600 | ~700 | 2011 | Now
ToxCast Phase II | 767 | ~600 | ~700 | 03/2013 | 10/2013
ToxCast Phase IIIa | 1001 | ~100 | ~100 | Just starting | 2014
E1K (endocrine) | 880 | ~50 | ~120 | 03/2013 | 10/2013
Tox21 | 8,193 | ~25 | ~50 | Ongoing | Ongoing
Chemicals
Assays
~600
~8,200
0
Data from ToxCast
Notes: It’s important to note that this is not just a data collection exercise. ORD has assembled the infrastructure to house, QA, and analyze the tens of thousands of data points.
AND make all of this data publically available.

## Slide 63
ToxCast phase I: primarily pesticides
ToxCast phase II: industrial chemicals
ToxCast phase III: diverse chemical space; high production
Data from ToxCast

## Slide 64
Data Endpoints
Chronic, developmental, acute toxicity endpoints:
Oxidative stress

## Slide 65
Adverse Oxidative Stress Pathways:
Diseases Associated with ROS
ROS = Reactive oxygen species

## Slide 66
KEap1 – nucleophile interaction
Toxicologic Pathology, 2007, 35:459–473,
Regulation of Nrf2-mediated gene transcription

## Slide 67
Trends in Pharmacological Sciences, 2013, 34, 6, 340-346
Keap1-Nrf2 Chemical inducers

## Slide 68
Study the physical, chemical and electronic properties of Keap1-Nrf2 inducers
Property-Based Approaches to Design Rules for Reduced Toxicity
Build a statistical quantitative model that relates computational parameters to adverse outcome pathways for oxidative stress.
Notes: Benzene diol to benzoquinone.

## Slide 69
Guidelines or rules that will allow chemists to rationally design chemicals that are unlikely to cause oxidative stress.
In vitro and in vivo toxicity studies of chemicals that are implicated in oxidative stress, including comparative studies.
MoDRN Key Deliverables:

## Slide 70
Hazard and Risk – Past and Present
Toxicology
Assessing Hazards and Exposure
  What Happens When You’re Exposed?
Hazard Minimization Through Molecular Design
QSAR - Quantitative Structure Activity Relationship
Molecular Design Research Network (MoDRN)
Topics Covered

## Slide 71
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE