## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Metrics
Image: Wikimedia Commons, Life Cycle Thinking, Author:The National Institute of Standards and Technology (NIST)
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 2: Conventional Metrics: Yield
The Algebra of Organic Synthesis: Green Metrics, Design Strategy, Route Selection, and Optimization, J. Andraos (2011), CRC Press

## Slide 3: By-product vs side product
target molecule
Point the side-product, and the by-product?
starting material
side-product
by-product

## Slide 4: By-product vs side product
 by-product of a reaction:
a product formed in the reaction between reagents as a direct mechanistic consequence of producing the target product assuming a balanced chemical equation that accounts for the production of the target product
side-product of a reaction:
a product formed in the reaction, usually undesired, arising form a competing reaction pathway other than the one that produces the intended target product
The Algebra of Organic Synthesis: Green Metrics, Design Strategy, Route Selection, and Optimization, J. Andraos (2011) CRC Press

## Slide 5: Conventional Metrics: Selectivity
Calvo‐Flores, "Sustainable chemistry metrics." ChemSusChem 2009, 2, 905-919.

## Slide 6: Conventional Metrics: Conversion
Calvo‐Flores, "Sustainable chemistry metrics." ChemSusChem 2009, 2, 905-919.
Yield = Conversion x Selectivity

## Slide 7: How Good Are The “Classic” Metrics?
How does classic metrics assess the following issues:
   the reaction is not quantitative
   there are unreacted starting materials
   I have some side product
   I produce by products
   I’m using solvent (in reaction, in work up)
   I’m using a catalyst (is it recovered?)
   I’m using auxiliaries
Calvo‐Flores, "Sustainable chemistry metrics." ChemSusChem 2009, 2, 905-919.

## Slide 8: How Good Are The “Classic” Metrics?
How does classic metrics assess the following issues:
   the reaction is not quantitative
   there are unreacted starting materials
   I have some side product
   I produce by products
   I’m using solvent (in reaction, in work up)
   I’m using a catalyst (is it recovered?)
   I’m using auxiliaries
Conversion
Conversion
Selectivity
Needs Green Metrics
Calvo‐Flores, "Sustainable chemistry metrics." ChemSusChem 2009, 2, 905-919.

## Slide 9: The Green Metrics
Materials efficiency:
 E-factor
 Atom economy
 Carbon efficiency
 E-factor based on molecular weight
 Effective mass yield
 Actual atom economy
 Environmental quotient
 Mass intensity
 Material recovery parameter
 Reaction mass efficiency
Energy efficiency:
 Energy intensity
 Waste treatment energy
 Solvent recovery energy
From: Calvo‐Flores, F.G. "Sustainable chemistry metrics." ChemSusChem 2009, 2, 905-919.
If you want even more: “The Algebra of Organic Synthesis: Green Metrics, Design Strategy, Route Selection, and Optimization”, J. Andraos (2011) CRC Press

## Slide 10: The Environmental Factor (E-Factor)
CHEM 462: 9. Atom Economy 1
Proposed by R. Sheldon in 1992
Notes: 10

## Slide 11
Classical synthesis of phloroglucinol.
Compound masses are expressed in gram per mol.
The Environmental Factor (E-Factor)

## Slide 12: Environmental Factor (E-Factor)
Depends on the definition of waste
  Non-recoverable starting materials, solvent, catalysts.
  Undesired side products.
Smaller E-factor means closer to zero waste
E-factor can be used to estimate/calculate the total waste generated:
Amount of Waste = Amount of Product x E-factor
Industry sector | Annual production (t) | E-factor | Waste produced (t)
Oil refining | 106-108 | Ca. 0.1 | 105 – 107
Bulk chemicals | 104-106 | <1–5 | 104 – 5 × 106
Fine chemicals | 102−104 | 5–50 | 5 × 102 − 5 × 105
Pharmaceuticals | 10–103 | 25–100 | 2.5 × 102 − 105
  E-factor = total waste (g) / product (g)
Notes: Different types of processes have different range of E-factor

## Slide 13: E-Factor Example
Friedel-Craft Alkylation (Substitution)
All numbers represent the mass of the chemical after the reaction.
Phenol | Chloroethane | Catalyst | Solvent | 4-Ethylphenol | 2-Ethylphenol | E-Factor
10 g | 20 g | 5 g | 1200 g | 80 g | 200 g | 6.575
  E-factor = total waste (g) / product (g)
 | At 10 g scale | 3-ton scale
Desired product | 200 g | 3 ton
Waste | 1315g | 19.725 ton
Industrial reactions are run on the big scale
Notes: (10+20+5+1200+80) / 200 = 6.575
0.020 / 0.007 / 0

## Slide 14: Process Mass Intensity (PMI)
CHEM 462: 9. Atom Economy 1
Mass Intensity = E-factor + 1
Notes: 14

## Slide 15: Atom Economy
CHEM 462: 9. Atom Economy 1
 atom economy is one of the 12 principles of green chemistry
 nowadays often used as a generic term to talk about maximizing conversion from starting materials into products
Atom economy demands to minimize the quantity of matter that will not be in the desired product at the end.
Moores A. “Atom economy, principles and a few examples." in Green Catalysis (2009) Wiley
Notes: 15

## Slide 16: Atom Economy: Example 1
Reagent | MW (g mol-1)
1 (Reactant) | 74.12
2 (Reactant) | 102.91
3 (Reactant) | 98.08
4 (Desired Product) | 137
CH3CH2CH2CH2OH + NaBr + H2SO4  CH3CH2CH2CH2Br + NaHSO4 + H2O
1 2 3 4 5 6 (Desired Product)
275.11 g mol-1
*including the stoichiometric coefficient
Notes: Reaction type??
137 / 275.11
49.8%

## Slide 17: Atom Economy: Example 2 - Ibuprofen Synthesis
From: Cann and Connelly “Real World Cases in Green Chemistry”, ACS: Washington, DC (2000)
The Problem:
The traditional industrial synthesis of ibuprofen was developed and patented by the Boots Company of England in the 1960s (U.S. Patent 3,385,886). This synthesis is a six-step process and results in large quantities of unwanted waste chemical byproducts that must be disposed of or otherwise managed. Much of the waste that is generated is a result of many of the atoms of the reactants not being incorporated into the desired product (ibuprofen) but into unwanted byproducts (poor atom economy/atom utilization). The process also uses a variety of solvents, and catalysts (if any) are not used in stoichiometric amounts.
The Solution:
The BHC Company has developed and implemented a new greener industrial synthesis of ibuprofen that is only three steps (U.S. Patents 4,981,995 and 5,068,448, both issued in 1991). In this process, most of the atoms of the reactants are incorporated into the desired product (ibuprofen). This results in only small amounts of unwanted byproducts (very good atom economy/atom utilization) thus lessening the need for disposal and mediation of waste products. There are other environmental advantages to the green synthesis versus the brown synthesis, including solvents and catalyst.

## Slide 18
Brown synthesis

## Slide 19
BHC synthesis

## Slide 20: Exercise: Calculate AE of the Greener Synthesis of Ibuprofen
BHC synthesis

## Slide 21: Exercise: Calculate AE of the Greener Synthesis of Ibuprofen
BHC synthesis

## Slide 22
Brown synthesis

## Slide 23: The Brown Synthesis of Ibuprofen
Brown synthesis

## Slide 24: The Brown Synthesis of Ibuprofen
Brown synthesis

## Slide 25
Ibuprofen
Synthesis
Brown synthesis
BHC synthesis
AE=40%
AE=77%

## Slide 26: Green Chemistry-Related Metrics Used in Chemical Manufacturing
Chemical manufacturer responses (n = 18) to the 2012 Roundtable Survey question “What green chemistry and engineering related metrics does your company use? Select all that apply.”
Percentage of respondents indicating one or more metrics surveyed in use computed as the ratio:
[total responses – (not sure + none)]/(total responses)
Implementing Green Chemistry in Chemical Manufacturing: A Survey Report
Giraud et al. ACS Sust. Chem. Eng. 2014, 2, 2237-2242.

## Slide 27
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE