## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Green Chemistry, principles and metrics
Image: Wikipedia, Biodegradation of nanocellulose, Author: Shaohui Li, Pooi See Lee
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 2
Topics To Be Covered
1. What is Green Chemistry?
2. The 12 Principles of Green Chemistry?
3. Designing chemicals products via Green Chemistry
4. Green Chemistry and the Market
5. Examples of the 12 principles


## Slide 3
Green chemistry is the design of chemical products and processes to reduce or eliminate the generation and use of hazardous substances.
Hazardous: to human health and to the environment
What is Green Chemistry?
Key reference: Anastas & Warner: “Green Chemistry: Theory & Practice” (1998, 2000)
Paul Anastas
(EPA)
John Warner (Polaroid Corp.)
Endavour started in 1990s…
Today embraced by researchers and industries around the world, including respectable chemical societies: Green Chemistry (1998)
impact factor: 8.6
impact factor: 30
Notes: Definition of the green chemistry: Green chemistry is the design of chemical products and processes that reduce or eliminate the use and generation of hazardous substances.
. The field was developed 25 years ago by Anastas and Warner, and presented in their seminal work “Green Chemistry: Theory and Practice”.

## Slide 4: 12 principles for Green Chemistry
P. Anastas, J. Warner in: Green Chemistry: Theory and Practice (New York, 1998).
 Waste Prevention
 Atom Economy
 Less Hazardous Chemical Syntheses
 Designing Safer Chemicals
 Safer Solvents and Auxiliaries
 Design for Energy Efficiency
 Use of Renewable Feedstocks
 Reduce Derivatives
 Catalysis
 Design for Degradation
Real-time analysis for Pollution Prevention
 Inherently Safer Chemistry for Accident Prevention

## Slide 5: How Often Are the 12 Principles Implemented in Chemical Manufacturing?
Survey done on chemical manufacturers contacted via The Nexus (ACS Green Chemistry Inst.)
Average chemical manufacturer responses (n = 17) to the 2012 Roundtable survey question:
“In your opinion, how frequently does your company implement the following principles of Green Chemistry?”
1: never (or not applicable)
2: rarely 3: regularly
4: fully
“Implementing Green Chemistry in Chemical Manufacturing: A Survey Report”; Giraud et al. ACS Sust. Chem. & Eng. 2014, 2, 2237-2242
Frequency of implementation of the 12 principles of Green Chemistry in chemical manufacturing.

## Slide 6: The Chemical Design Process
Ultimately determines characteristics of the waste stream, energy requirements, and toxicity of the entire process.
DECISION MAKING
Type of resources
What materials (feedstocks, additives) are needed?
Are the materials readily available?
How much material is needed?
Manufacturing process
What technology is needed?
What is the scale of the experiment? (big companies operate ata different scale than a startup)
Feedstocks are important, but at the design phase decisions must be made on solvents, additional reactants, auxiliaries, catalysts
Notes: Types of resources:
While the starting materials are important (feedstocks), at the design phase the decision on the solvents, additional reactants is also necessary.
Decision on the scale of the manufacturing process is needed. Each industry is different, for example a big pharma will have other scale than a startup.
All these decisions determine the characteristics of the waste streem, energy usage, and toxicity of the entire process.

## Slide 7: Let us look at functional organic polymers
 Solubility (manufacturing)
 Melting point (manufacturing, resource)
 Glass transition temperature (manufacturing, resource)
 Mechanical properties (tensile strength, modulus etc)
 Refractive index
 Surface Tension
 Yields/selectivity
Image: HP
Conventional criteria important for the Chemical Design of a new product

## Slide 8: Green Chemistry-Inspired Design Criteria
 Solubility (manufacturing)
 Melting point (manufacturing, resource)
 Glass transition temperature (manufacturing, resource)
 Mechanical properties (tensile strength, modulus etc)
 Refractive index
 Surface Tension
Yields/selectivity
Toxicity
 Environmental impact
Green Chemistry perspective is not far from what’s currently being practiced.
It is simply considering hazards at the inception of product development that makes it a powerful tool.
Image: Philips

## Slide 9: Focus on Chemical Design
The moment chemists begin to design, they are making choices about the health and environmental impacts of their product:
Design is intentional.
All characteristics, including performance and toxicity, can be designed.
Image source: ChemDoodle Web Components

## Slide 10: Green Chemistry Across Industrial Sectors
Defense and aerospace
Adhesives
Coatings
Corrosion, inhibitors
Electronics
Solder
Housings
Displays
Automotive
Solvents
Polymers
Fuels
Household cleaners
Surfactants
Fragrances
Dyes
Agriculture
Pesticides
Fungicides
Fertilizers
Cosmetics
Builders
Chelating agents
Dyes
Pharmaceuticals

## Slide 11: Pharmaceutical Industry

## Slide 12: Green Chemistry Innovation in Other Fields
clothing
home & garden
Entertainment
building materials
Image source: Wikipedia
Electronics
New materials for storage/transport of silanes, germanes, arsine etc. (NuMat, Inc.)
cleaning products
food products
jewelry
and more!

## Slide 13: Benefits of Green Chemistry
For the environment:
  Products will biodegrade and will not persist in the environment.
  Products & processes will not cause toxic harm to humans (employees, consumers)
  Novel products can boost competitiveness
Products made from renewable, abundant resources.
  Fundamental new insights
For human health:
For the economy:
For sustainability:
For science:

## Slide 14: Green Chemistry Market Predictions
Forecasted market size of Green Chemistry industry worldwide from 2015 to 2020 (US$B)
Calculated based on the compound annual growth rate (CAGR) of 10.6 between 2015 and 2020, as stated by the source. Figures from 2016 to 2020 are forecasted.
Source: statista.com
“CleanTech”

## Slide 15: Growing Demand & Planning for “Greener” Chemicals
“The companies were driven less by idealism than by intense competition, and a bet that they could create more environmentally friendly alternatives.”
http://www.nytimes.com/2016/10/17/business/how-the-chemical-industry-joined-the-fight-against-climate-change.html?_r=0
Global Warming Potential (GWP) Comparison
In 2006, EU adopts the Mobile Air Conditioning (MAC) Directive to reduce climate impact of air conditioning in cars sold in the EU.
Effective in 2011 MAC Directive requires an automotive refrigerant with a GWP below 150.
 September 2016: New York Declaration urged a global reduction in the use of HFCs
 October 2016: negotiators from 197 nations at the summit of the UN Environment Programme (Kigali, Rwanda) reached a legally-binding amendment to the Montreal Protocol, to phase out HFCs.
Next day, Honeywell and Chemours (DuPont spin-off) actively backed regulations and moved towards more environmentally friendly refrigerants. (New York Times, 16/10/2016)
“How the Chemical Industry Joins the Fight Against Climate Change?”
The development of HFC alternatives started in early 2000s

## Slide 16: But, Isn’t That How it is Done Now?
 Entire industries are geared toward cleaning up after wasteful chemical syntheses.
 Scientific literature is filled with synthetic pathways that are inefficient in terms of design.
 Reagents are seldom selected with regard to hazard.
 Industrial chemicals do not have minimal hazard as a performance criterion.
 Persistence of chemicals in the biosphere and in our bodies is a major global health issue (CDC 250 chemicals since 1945).
 The vast majority of organic chemicals are made from depleting (non-renewable) feedstocks (petrochemicals!).
 Our chemical industry deals with safety through engineering and security through barricades.

## Slide 17: Dealing with Risk: Exposure vs Design
Green chemistry focuses on reducing risk by reducing hazard.
- If there is no hazard, exposure becomes irrelevant!
The conventional approach to hazards focuses, for example, on reducing risk by minimizing exposure.
- wearing personal protective equipment or space ventilation if the chemical is volatile.
If we can master the design and synthesis of molecules, why don’t we aim it toward eliminating hazards?

## Slide 18: Green Chemistry: A Change in Perspecyive
Hazard must be recognized as a flaw in the designing process.
circumstantial
(depends on situation)
   use
   exposure
   handling
   treatment
   protection
   recycling
   costly
intrinsic (inherent in design)
   molecular design for reduced toxicity
   reduced ability to manifest hazard
   inherent safety from accidents or terrorism
   increased potential profitability
Green Chemistry moves our consideration of how to deal with environmental problems from the circumstantial to the intrinsic.

## Slide 19: Another Design Principle: Function vs Molecule
Green Chemistry also rethinks the problem de novo. We move from considering the molecule/material to the function.
Thinking about function calls for interdisciplinary research to “think outside the box”
molecules/materials
   bisphenol A/phtalates
   epoxy resins
   Cisplatinum
   polyethylene terephthalate (PET)
   dichloromethane
function
   plasticizing
   coating
   catalyst
  materials which can be molded, do not leak..
   solvent

## Slide 20: Traditional approach
more environmentally
benign than alternatives
performs better
than alternatives
more economical
than alternatives

## Slide 21
safety
performance
cost
Green
Chemistry
Holistic approach

## Slide 22
1. Waste Prevention
2. Atom Economy
3. Less Hazardous Chemical Synthesis
4. Designing Safer Chemicals
5. Safer Solvents and Auxiliaries
6. Design for Energy Efficiency
7. Use of Renewable Feedstocks
8. Reduce Derivatives
9. Catalysis
10. Design for Degradation
11. Real-time Analysis for Pollution Prevention
12. Inherently Safer Chemistry for Accident Prevention
Anastas, Warner; Green Chemistry: Theory and Practice, Oxford University Press (1998)
The 12 Principles of Green Chemistry
Notes: Green chemistry is defined by 12 Principles, which address various topics. Most principles have tools or metrics associated to help the researcher and guide them through green chemistry improvements.

## Slide 23: What is waste?
Waste is anything that is a leftover from the product/process and cannot be re-used.
Waste can be produced in any stage of a process life-cycle:
 origins of feedstock
 manufacturing
 distribution
 use
 end of life
When is waste NOT waste?
 when it can be reused, becoming a feedstock.
 When it can be reduced or completely eliminated.
Waste Prevention

## Slide 24
Waste Prevention
Case study: Sildenafil citrate production - Pfizer
Sildenafil citrate, commonly known as Viagra, is a selective inhibitor of phosphodiesterase 5 (PDE5). Sales > $1 billion during its first year on the market.
With such a rapid sales take off it was critical that the environmental performance of the synthesis was good from the outset!
Conventional sildenafil citrate synthesis included:
 11 steps for a 4.2% overall yield.
 SnCl2, heavy metal and major environmental polluter.
 stoichiometric thionyl chloride (SOCl2) in a solvent. This has a high environmental impact.
 hydrogen peroxide: burns upon skin contact, fire and transportation hazard, especially in contact with organic matter
 over 1300 L waste per kilogram of product.
Organic waste produced by sildenafil citrate processes at various time points
Dunn et al. Green Chem. 2004, 6, 43-48

## Slide 25
Waste Prevention
Alternative production of sildenafil citrate:
 average yield of last three steps = 97% yield.
 7 L/kg by minimizing solvent use, increasing solvent recovery, better solvent choice, and telescoping steps.
 only the solvents tert-butanol, ethyl acetate, 2-butanone, and a trace of toluene still require disposal.
Dunn et al. Green Chem. 2004, 6, 43-48
Pfizer, Inc

## Slide 26
Atom Economy
In 1990 Barry Trost introduced a concept of synthetic efficiency: Atom Economy (AE)
It refers to the concept of maximizing the use of raw materials so that the final product contains the maximum number of atoms from the reactants.
An ideal reaction would incorporate all of the atoms of the reactants.
The AE is measured as the ratio of the molecular weight of the desired product over the molecular weights of all reactants used in the reaction.
Additional considerations when designing a green reaction:
 generation of co-products and waste
 toxicity of co-products and waste
 energy needs
 purification steps
 solvent and catalyst use
Barry Trost

## Slide 27
Atom Economy
USE YOUR ATOMS!!!!

## Slide 28
Atom Economy
Synthetic methods should be designed to maximize the incorporation of all materials used in the process into the final product.
Image: Wikimedia Commons, Author: Astrid 91

## Slide 29
Conventional synthesis of ibuprofen:
   six stoichiometric steps
   below 40% atom utilization
Atom Economy: Ibuprofen

## Slide 30
Alternative catalytic synthesis of ibuprofen:
 3 catalytic steps
 80% atom utilization
  BHC
Atom Economy : Ibuprofen

## Slide 31
Less Hazardous Chemical Synthesis
Synthetic methodologies should be designed to use and generate substances that possess little or no toxicity to human health and the environment.
Image: Wikimedia Commons, Center for Biofilm Research Laboratory Montana State University

## Slide 32
Case study: Synthesis of adipic acid
 one of the most produced commodity chemicals worldwide
 projected global market size >US$ 7 billion by 2019
 versatile building block in chemical, pharmaceutical and food industries
 precursor for the synthesis of the polyamide Nylon-6,6.
Conventional synthesis:
 benzene, a known carcinogen, is a starting material
 oxidation with excess of HNO3, production of nitrous oxide (N2O) a GHG (5–8% of worldwide anthropogenic N2O emissions).
Less Hazardous Chemical Synthesis

## Slide 33
Alternative synthesis of adipic acid:
Less Hazardous Chemical Synthesis
Check out: Raj et al. “Biocatalytic production of adipic acid from glucose using engineered Saccharomyces cerevisiae” Metabolic Engineering Communications. 2018, 6, 28-32.
 development of biocatalytic processes for producing adipic acid and catechol from sugars.
 biocatalytic process using yeast converts sugars to cis,cis-muconic acid, and this intermediate stage allows ready access to catechol and adipic acid.
 uses water as solvent at ambient temperature and pressure.

## Slide 34
Designing Safer Chemicals
Chemical products should be designed to preserve efficacy of the function while reducing toxicity.

## Slide 35
“Everything is toxic. It is simply depends on the dose”
Often otherwise phrased as
“The dose makes the poison.”
Risk = Hazard x Exposure
Designing Safer Chemicals
Green chemistry and engineering focus on reducing risk by reducing hazard.

## Slide 36
Hazard types to avoid:
  Toxicological/Eco-toxicological
    Carcinogenicity
    Reproductive
    Developmental
    Neurological
    Global warming potential
    Ozone depleting potential
    Bioaccumulation
    Persistence
  Physical
    Explosivity
    Flammability
    Corrosivity
Physical/Chemical Properties to consider:
  Water solubility
  Log Kow
  Volatility
  Molar volume
  Aspect ratio
  Radical formation
  Nucleophilicity
  Electrophilicity
  pH/pKa
  Surface area
  Reducing potential
  Oxidizing potential
  Polarizability
Designing Safer Chemicals

## Slide 37
Conventional use of organotin compounds as antifoulants:
 TBTO and related antifoulants have long half-lives in the environment (the half-life of TBTO in seawater is >6 months).
 they bioconcentrate in marine organisms (the concentration of TBTO in marine organisms has been found to be up to 104 times greater than in the surrounding water).
 organotin compounds are chronically toxic to marine life and can enter food chain. Extreme neurological hazard.
 bioaccumulative
tributyltin oxide (TBTO)
Case study: Antifoulants
Designing Safer Chemicals
Antifoulants are generally dispersed in the paint as it is applied to the hull. Organotin compounds such as tributyltin oxide (TBTO) have traditionally been used: gradually leaches from the hull, killing the fouling organisms in the surrounding

## Slide 38
Alternative antifoulants (Dow Chemicals):
 Sea-Nine® 211 (DCOI) works by maintaining a hostile growing environment for marine organisms
 when organisms attach to the hull treated with DCOI, proteins at the point of attachment react with the DCOI
 reaction with DCOI prevents the use of these proteins for other metabolic processes: organism detaches itself and searches for a more hospitable surface to grow upon.
 Only organisms attached to hull of ship are exposed to toxic levels of DCOI.
 readily biodegrades once leached from ship (half-life is less than one hour in sea water).
Case study: Antifoulants
Designing Safer Chemicals
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-1996-designing-greener-chemicals-award
Awardee in 1996

## Slide 39
Solvents account for the vast majority of mass wasted in syntheses and processes. Moreover, many conventional solvents are toxic, flammable, and/or corrosive.
Solvents volatility and solubility have contributed to air, water and land pollution, have increased the risk of workers’ exposure, and have led to serious accidents.
Recovery and reuse, when possible, is often associated with energy-intensive distillation and sometimes cross contamination. In an effort to address all those shortcomings, chemists have started to search for safer solutions.
Safer Solvents and Auxiliaries

## Slide 40
Problematic organic solvents
avoidance
environmentally
benign and safe
easily separable, safe
zero
volatility
greener alternatives
Safer Solvents and Auxiliaries
no solvent
supercritical fluids
ionic liquids
water solvent

## Slide 41
Zoloft® is an anti-depressant; once one of the best selling pharmaceuticals on the market.
Conventional sertraline synthesis:
 synthesis was a three step process.
 used 4 hazardous solvents (methylene chloride, tetrahydrofuran, toluene, and hexane).
Zoloft®
Safer Solvents and Auxiliaries
Case study: Manufacturing process for sertraline, the active ingredient in the popular drug Zoloft®

## Slide 42
 process was streamlined to a single step, carried out in ethanol, a much less toxic solvent.
 new process is catalytic, cutting down on starting materials by 60%, 45%, and 20% for the three reaction components.
 combined steps eliminated 180 tons of TiCl4, 150 tons of 50% NaOH, 180 tons of 35% HCl waste, and 600 tons of solid TiO2.
Pfizer, Inc
Case study: Manufacturing process for sertraline, the active ingredient in the popular drug Zoloft®
Alternative sertraline synthesis:
Safer Solvents and Auxiliaries
Image: Wikimedia Commons, Author: Ragesoss

## Slide 43
Design for Energy Efficiency
Energy requirements should be recognized for their environmental and economic impacts and should be minimized.
Synthetic methods should be conducted at ambient temperature and pressure.

## Slide 44
Most energy is used for heating, cooling, separations and pumping.
Ideally, all reactions are performed at ‘ambient’ conditions – room temperature and atmospheric pressure – in order to minimize energy usage.
Design for Energy Efficiency
Image: Wikimedia Commons, Janicki Omni Processor Pilot Plant in Dakar, Senegal , Author: Janicki Bioenergy

## Slide 45
Atorvastatin, a cholesterol-lowering drug (Lipitor), suffers from an energy-demanding synthesis as a result of two cryogenic reactions at - 70 oC
New biocatalytic synthesis uses enzyme DERA and shortens the process by removing two energy intensive chemical steps.
Case Study: Atorvastatin
Design for Energy Efficiency
DERA: deoxyribose-5-phosphate aldolase
CBzNH
CBzNH
DERA

## Slide 46
Use of Renewable Feedstocks
A raw material or feedstock should be renewable rather than depleting whenever technically and economically practical.
Image: Wikipedia, Pongamia Pinnata Seeds

## Slide 47
Case study: Production of levulinic acid
 precursor for pharmaceuticals, plasticizers, and various other additives
 widely used as a building block/starting material
Conventional synthesis:
 made by heating hexoses (glucose, fructose) or starch in dilute HCl or H2SO4
 yield depends on acid, its concentration, temperature, pressure
 reaction also produces hard to remove by-products.
Use of Renewable Feedstocks
fructose
hydroxymethylfurfural (HMF)
formic acid
levulinic acid

## Slide 48
paper mill
sludge
levulinic acid
municipal solid waste
and waste paper
agricultural
residues,
waste wood
Alternative synthesis:
 levulinic acid can be obtained from paper mill sludge, agricultural and municipal waste and paper.
 uses a high-temperature, dilute-acid hydrolysis process that converts cellulosic biomass.
Biofine, Inc
Use of Renewable Feedstocks
Case study: Production of levulinic acid
hydrolysis

## Slide 49
Reduce Derivatives
Unnecessary derivatization (blocking group, protection/deprotection, temporary modification of physical/chemical processes) should be avoided whenever possible.
Image: Wikimedia Commons, Center for Biofilm Research Laboratory Montana State University

## Slide 50
Substrate
Product
Substrate
Intermediate A
Intermediate B
Intermediate C
Intermediate D
Intermediate E
Product
Conventional approach
Green Chemistry approach
Reduce Derivatives
Notes: Whenever possible, limit number of steps and unnecessary transformations. Avoid the use of protecting groups as it requires extra reagents and generates more waste.

## Slide 51
6-APA: core moiety of penicillin
Conventional synthesis of 6-aminopenicillanic acid using 3 steps and intermediates:
Alternative synthesis using enzyme and fewer derivatives:
Case study: 6-aminopenicillanic acid (6-APA)
Reduce Derivatives

## Slide 52
Catalysis
Catalytic reagents (as selective as possible) are superior to stoichiometric reagents.
Image: Flickr, Catalysts, Author: BASF Catalysts

## Slide 53
Catalysts can facilitate complex reactions by:
lowering the activation energy (Ea) of the reaction.
 reducing temperature necessary to achieve a reaction.
 controlling the site of the reaction (selectivity enhancement).
 catalysis is a cyclic event
Image source: Adobe stock
Catalysis
I. Chorkendorff, J. W. Niemantsverdriet, Concepts of Modern Catalysis and Kinetics, Wiley-VCH, 2003
Notes: Catalysts lower the activation (threshold energy) in the reaction.

## Slide 54
Many molecules/enzymes/materials can be catalysts
Catalysis
Catalysis, Concepts and green applications, by Gadi Rothenberg, Wiley-VCH 2008.
copper-zinc crystallites on silica
zeolite (crystalline alumosilicate)
enzyme (biocatalyst)

## Slide 55
  Dartt and Davis
  97% yield in three steps
Nonsteroidal anti-inflammatory drug (NSAID) of the propionic acid class (the same class as ibuprofen) that relieves pain, fever, swelling, and stiffness; COX inhibitor
Catalysis: Green Naproxen Synthesis
Notes: cyclooxygenase

## Slide 56
Design for Degradation
Chemical products should be designed so that at the end of their function they do not persist in the environment and instead break down into innocuous degradation products.
Image: Wikicommons, a landfill in Dryden, Ontario, Author: Michelle Arseneault

## Slide 57
Early examples of non degrading products:
  sulfonated detergents
   alkylbenzene sulfonates – 1950’s & 60’s
     foam in sewage plants, rivers, and streams
     persistence was due to long alkyl chain
     introduction of an alkene group into the chain increased degradation
  chlorofluorocarbons (CFCs)
     do not break down, persist in atmosphere and contribute to destruction of the ozone layer.
  DDT
     bioaccumulate and cause thinning of egg shells
Design for Degradation

## Slide 58
Conventional plastics (e.g. PET) are made from petroleum:
 PET Plastic persists in the environment
 made from depleting resources
high temperature
vacuum
catalyst
petroleum product
Design for Degradation: PLASTICS

## Slide 59
Synthesis of PolyLactic Acid (PLA) from starch:
 a biobased, compostable, and recyclable PLA polymer that uses 20–50 percent less fossil fuel resources than comparable petroleum-based polymers.
 the first family of polymers derived entirely from renewable resources that can compete cost-effectively with traditional fibers and plastic packaging materials.
 manufacturing process consists of three solvent-free steps that lead to the production of lactic acid, lactide, and PLA high polymer with very high yields and internal recycling schemes that reduce waste.
 PLA can be biodegraded under industrial compositing conditions - does not degrade though in the environment
Cargill Dow LLC
Design for Degradation: PLASTICS
Alternative process:

## Slide 60
Real-time Analysis for Pollution Prevention
Analytical methodologies need to be further developed to allow for real-time in-process monitoring and control prior to the formation of hazardous substances.

## Slide 61
Real time analysis for a chemist is the process of “checking the progress of chemical reactions as it happens”.
Knowing when your product is “done” can save a lot of waste, time, and energy!
Image: Wikimedia Commons
Real-time Analysis for Pollution Prevention

## Slide 62: What Does Green Analytical Chemistry Mean?
Green Chemistry is applicable to all chemical processes, including the methods, protocols and processes of analytical chemistry.
Image: Wikipedia
Real-time Analysis for Pollution Prevention

## Slide 63: Examples of Green Analytical Chemistry Methodologies
X-ray fluorescence detection for multi-metal matrix
Image Sources: https://www.thermofisher.com, https://www.intechopen.com/books/herbicides-advances-in-research/recent-advances-in-the-extraction-of-triazines-from-water-samples, J. P. McMullen, M. T. Stone, S. L. Buchwald and K. F. Jensen, Angew. Chem., 2010, 39, 7230
Desired product
In-line HPLC analyzer, on flow
Real-time adaptation of addition of 1 and 2 to max. 3
Real-time Analysis for Pollution Prevention

## Slide 64
In 2008 Naclo Company won the EPA Greener Reaction Conditions Award for their innovative 3D TRASAR® Technology.
Case study: Real-time analysis in cooling systems
Alternative Cooling System with 3D TRASAR® Technology:
3D TRASAR® System allows for the real-time monitoring of mineral scale buildup.
system can also utilize poor-quality water.
3D Scale Control prevents mineral scale formation to increase efficiency.
3D Bio-control performs a real-time check for planktonic and sessile bacteria. This reduces the amount of biocide used since biocides are then added only when necessary, rather than on a set schedule.
3D TRASAR® System greatly reduces the amount of wastewater discharged from cooling systems.
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-2008-greener-reaction-conditions-award
Image: Wikipedia, A lavender-colored nonpotable water pipeline in Mountain View, California, Author: Grendelkhan
Real-time Analysis for Pollution Prevention
Notes: The system monitors antiscalant levels using a fluorescent-tagged, scale-dispersant polymer and responds quickly when conditions favor scale formation. In addition, 3D Bio-control, also part of the 3D TRASAR® system, is the only online, real-time test for measuring planktonic and sessile bacteria. It uses resazurin, another fluorescent molecule, which changes its fluorescent signature when it interacts with respiring microbes. By adding an oxidizing biocide in response to microbial activity, 3D Bio-control generally reduces the use of biocide and also prevents biofilm from building up on surfaces, maintaining efficient heat transfer.

## Slide 65
Inherently Safer Chemistry
for Accident Prevention
Substance and the form of a substance used in a chemical process should be chosen so as to minimize the potential for chemical accidents, including releases, explosions, and fires.
Image: Flickr, Author: sea turtle

## Slide 66
approaches to design safer chemistry can include the use of solids or low vapor pressure substances in place of volatile liquids.
 other approaches include avoiding the use of molecular halogens in large quantities.
 continuous flow processes can help to minimize chemical hazards.
Accidents can be avoided by minimizing hazards
Inherently Safer Chemistry
for Accident Prevention

## Slide 67
Case study: Production of gasoline alkylate with AlkyClean® Technology
In 2016 Albemarle and CB&I won the EPA Green Chemistry Award for their inherently safer AlkyClean® process technology.
AlkyClean® Technology:
 AlkyClean® solid acid alkylation process produces high quality alkylate without using liquid acid catalysts.
 solid acid alkylation process is safer for both people working directly in production and for people in the area surrounding the facility.
 environmental and economic benefits since no acid-soluble oils or spent acids are produced.
Conventional alkylate production:
 alkylate is typically produced from the reaction of isobutane and light olefins.
 requires the liquid acid-catalyzed processes, such as hydrofluoric acid.
 hydrofluoric acid is extremely toxic, upon release it forms clouds that can be lethal for up to five miles.
Inherently Safer Chemistry
for Accident Prevention

## Slide 68: More examples available!
Presidential Green Chemistry Challenge Winners
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-winners
How Industrial Applications in Green Chemistry Are Changing Our World (white paper) by American Chemical Society
Inherently Safer Chemistry
for Accident Prevention

## Slide 69
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE